## Slide 1
WHAT IS A JETSON? · NVIDIA, 2020
Jetson Nano 2GB
A $59 mini computer built to teach AI and robotics. No longer sold, still very capable.
My use: DATV on QO-100
Its hardware H.265 encoder feeds an ADALM-Pluto
CPU
4-core ARM Cortex-A57, 1.43 GHz
GPU
128-core NVIDIA Maxwell, CUDA
RAM
2 GB LPDDR4, shared with GPU
VIDEO
H.264 / H.265 hardware encoder
I/O
Gigabit LAN, 3× USB, HDMI
POWER
5 V USB-C, about 5–10 W
OS
Ubuntu 18.04 + JetPack 4.6
Notes: What is a Jetson Nano 2GB: NVIDIA's $59 AI learning kit from 2020, now end of life. Key point for DATV: the hardware H.264/H.265 video encoder, which feeds the ADALM-Pluto for QO-100.

## Slide 2
READY-TO-FLASH SD CARD IMAGE · HB9IIU
Got a Jetson Nano 2GB in a drawer?
Never managed to make it work? Turn it into a DATV transmitter.
Works out of the box with a Pluto
ADALM-Pluto running Evariste's (F5OEO) firmware
USB camera is optional
Plug in a webcam for live pictures, or run without one
Demo video included
Something to transmit from the very first boot
Add your own videos
Upload more clips from any browser via the web UI
3 clicks
to go on air
1
Select source
2
Pick a free BATC slot
3
Start stream
Notes: Many of us have a Jetson Nano 2GB lying in a drawer - I did too, and never really got it working. This SD card image turns it into a DATV transmitter: flash it, connect a Pluto with Evariste's firmware, and you're ready. A USB camera is optional, a demo video is included, and you can upload your own clips from the web UI. Going on air takes three clicks: select a source, pick a free slot on the BATC spectrum, start stream.

## Slide 3
Get the SD card image
FREE DOWNLOAD · RASPBERRY PI IMAGER · 32 GB CARD
Scan the code, flash the card, boot the Jetson.
Download the image
Scan the QR code: jetson.img.xz, about 5.6 GB
Use a 32 GB microSD card
Tested and working on a fresh 32 GB card
Flash with Raspberry Pi Imager
Choose OS › Use custom › jetson.img.xz (no unzip)
Boot and open the web UI
Power up, then browse to http://jetson-nano.local
Scan to download
Google Drive · jetson.img.xz
Notes: Download link: https://drive.google.com/file/d/1KOO9mWcRhIP5yVT3PENrq5p7Ek5pGANZ/view?usp=sharing Flash with Raspberry Pi Imager (Choose OS > Use custom) onto a 32 GB microSD card. Tested and working.